## Slide 1
WEEK 04
P R O J E C T W O R K
Weekly Progress
Report
Recycling Injection Machine & 3D Printed Tool Optimization
P A R T N E R
Plastic Cup
(PET Kupa)
D A T E
10 March 2026
P H A S E
Mold Inspection
Budapest University of Technology and Economics · Dept. of Machine and Product Design · Dr. Viktor Gotthard
• Abed Alrahman Marai • Emir Sukru Birdal • Bashar Darwazeh • Ingynn Khet • Nomin-Erdene Tsogt

## Slide 2
WEEK 04 AGENDA
01
Week 4 Progress
Inspection recap, defects found, design limitations
02
Existing Mold & Inserts
Documentation of mold system components
03
Identified Design Issues
Printing defects, fit problems, sprue location
04
Preliminary Improvements & Next Steps
Redesign directions and upcoming tasks
Project Work · Week 04 · BME GT3

## Slide 3
04 | Week 4 Progress
✓ COMPLETED THIS WEEK
Physical inspection of injection mold and mold inserts
Documentation of defects reported by industrial partner
Comparison of FDM and photopolymer printing methods
Partner discussion: injection channel configuration
Identification of design limitations in current mold
Initial redesign concept directions established
→ TASKS FOR WEEK 05
Detailed defect analysis
Measure tolerances, document surface quality issues
CAD redesign of mold inserts
Revised geometry for improved fit and print quality
Adapter / spacer plate design
Reduce required insert thickness, save material
Injection channel redesign
Relocate sprue to top mold component
Project Work · Week 04 · BME GT3

## Slide 4
Existing Mold and Inserts
The team physically inspected and documented the full mold system during the Week 04 partner session. Images and measurements were recorded for each component below.
Mold Casing
[ Photo Placeholder ]
Outer housing containing the mold inserts. Current depth assessed for redesign.
Mold Inserts
[ Photo Placeholder ]
3D-printed inserts forming the part cavity. Surface defects and fit issues documented.
Assembled Mold
[ Photo Placeholder ]
Full assembly with inserts seated in casing. Alignment and sprue position reviewed.
Project Work · Week 04 · BME GT3

## Slide 5
Current Injection Configuration
CURRENT SETUP
Sprue is located on the surface of the mold insert
Injection occurs directly from the insert face
Requires alignment of nozzle with insert surface
Limits flow path design options within the mold
Increased risk of leakage at the insert parting line
[ Current sprue position – photo placeholder ]
→
PROPOSED CONFIGURATION
Industrial partner suggested injecting from the top mold component
Sprue relocated to top surface of upper mold half
Improved flow direction into the mold cavity
Potentially reduces flash and incomplete fills
Better alignment between machine nozzle and sprue gate
To be validated through CAD redesign and testing
[ Proposed sprue position – diagram placeholder ]
Project Work · Week 04 · BME GT3

## Slide 6
Identified Design Issues
Issue 1
3D Printing Defect on Mold Insert
Visible line crossing the insert surface
Likely caused by layer shift or print pause
May affect surface quality of molded parts
Issue 2
Poor Fit Between Insert and Mold Casing
Insert does not seat properly inside housing
Possible misalignment during assembly
May cause flash or leakage under pressure
Issue 3
Excessive Mold Casing Depth
Current casing requires unnecessarily thick inserts
Leads to increased print time and material use
Adapter plate proposed to reduce insert thickness
Issue 4
Sprue Location on Insert Surface
Current sprue gate on insert face causes alignment issues
Partner suggested top-injection configuration
Redesign of injection channel required
Project Work · Week 04 · BME GT3

## Slide 7
Preliminary Improvement Ideas
Print Quality
Optimise FDM print settings (temperature, speed, layer height)
Evaluate high-temp filament options (e.g. ABS, ASA)
Add post-print sanding or surface treatment to inserts
Consider resin printing for critical cavity surfaces
Insert & Casing Fit
Revise insert dimensions to improve housing tolerance
Add alignment features (pins, slots) to prevent misassembly
Design adapter / spacer plate to reduce insert material
Reduce casing depth to match optimised insert thickness
Injection Channel
Relocate sprue gate to the top mold component
Redesign flow channel for better fill direction
Add venting to reduce trapped air and short shots
Prototype and test revised channel with HDPE material
Project Work · Week 04 · BME GT3

## Slide 8
04 | Tasks for Next Week
✓ COMPLETED THIS WEEK
Mold and insert physical inspection
Defect documentation with industrial partner
FDM vs photopolymer printing comparison
Injection channel configuration review
Identification of four key design issues
Preliminary improvement directions established
→ TASKS FOR WEEK 05
Detailed Defect Analysis
Measure tolerances, document all surface quality issues quantitatively
CAD Redesign – Mold Inserts
Revised insert geometry for improved fit and printability
Adapter / Spacer Plate Design
Reduce required insert thickness to save material and print time
Injection Channel Redesign
Relocate sprue to top mold component per partner specification
Mold Testing Preparation
Coordinate with industrial partner for test injection session
Project Work · Week 04 · BME GT3